# Knovative & Coast CATV Equipment Supply

# Where Knowledge Drives Innovation

## KCMTS-122

### DOCSIS CompactCMTS

Knovative’s CompactCMTS is a high-performance, cost-effective and highly integrated DOCSIS Cable Modem Termination System (CMTS).  The CompactCMTS is a complete, self-contained DOCSIS CMTS.  With its internally integrated Upconverter, DHCP, TFTP and TOD servers everything needed to support DOCSIS cable modem operation is provided.  Its compact size and highly integrated design makes the CompactCMTS the most ideal CMTS product for Franchised Cables and for Private Cables, MDUs, SMTVs, campuses and hotel operations.

Knovative offers two models of CompactCMTS.  The KCMTS-122 complies with DOCSIS and KCMTS-122E complies with EuroDOCSIS.  Both models are delivered with software that is fully DOCSIS 1.0 compliant and supports the most frequently used DOCSIS 1.1 features.

Both KCMTS-122 and KCMTS-122E support one downstream and two upstream channels.   The mechanical design allows it to be installed on a 19” rack or table/tray (with rack mounting handles removed).  All interface cables and LED status indicators are located at the front for easy wiring.

Front View

KCMTS-122, KCMTS-122E Interfaces, Features and Functions

Front Panel Interfaces

- Downstream Output – Provides the QAM64 or QAM256 modulated DOCSIS downstream data.

- Downstream Monitor – for examining the downstream RF signal without interfering with the normal downstream RF signal.

- US1 Input, US2 Input – Accepts QPSK or QAM16 modulated DOCSIS upstream data.

- US1 Monitor, US2 Monitor – for examining the upstream RF signal without interfering with the normal upstream RF signal.

- Network – 10/100BaseT Ethernet (DCE) port that carries data and management packets between the CMTS and the backbone network.  Both internal Web Server and Telnet are available through the Console port for accessing the internal DHCP, TFTP servers and CompactCMTS data base for Cable Modem provisioning.

- Console – RS232 serial port for monitor and control of the CompactCMTS using the same commands provided by Telnet.  This port can be attached to a standard phone modem for continued access during network connection outages.

Features and Functions

##### Downstream

- Provides downstream signal at DOCSIS frequency range. There is no need for external upconverter.

- Fully compliant to DOCSIS downstream PHY layer and MAC layer specifications.

- Supports and compliant to DOCSIS BPI/BPI+ security specifications.

Upstream

- Fully compliant to DOCSIS upstream PHY layer specifications including channel equalization.

- Fully compliant to DOCSIS upstream MAC layer specifications including MAP generation, UCD generation, cable modem ranging, MAC de-framing, frame error detection, MAC message extraction and PDU frame deconcatenation.

- Supports and compliant to DOCSIS BPI/BPI+ specifications.

Network

- Layer-2 bridging, supports DOCSIS spanning-tree protocol.

- Flexible CM provisioning using either internal DHCP, TFTP servers or optional external servers.

- Built-in Time-of-Day server for cable modem support.

- Supports DOCSIS IGMP Proxy and IP Multicast.

Operational Support System (OSS)

- Native CMTS control/status

  - Intuitive built-in Web Server.  Use standard Internet Explorer or other web browser to access.  Different access control groups for monitoring, setup or administration.

  - SNMP MIBI/II access supports both DOCSIS standard and Private MIBs.

  - Telnet access

  - Consol port access

- Provisioning similar to DOCSIS cable modem provisioning

- DHCP client retrieval of CMTS IP address, handle to CMTS configuration file.

- TFTP client retrieval of CMTS configuration file, software/firmware update files.

- Internal DHCP, TFTP and Time of Day Servers make this a standalone system.  DHCP can provide either IP address pools or static IP address assignment to both CMs and CPEs.

- Provisioning can also forward DHCP/TFTP to external servers in full compliance with DOCSIS requirements.

KCMTS-122, KCMTS-122E Specifications

| Downstream Physical Layer |
| --- |
| Quantity of downstream channel | 1 |
| Modulation type | 64 and 256 QAM (ITU-T J.83 Annex B) |
| Frequency Range | 88 to 860 MHz (KCMTS-122) 108 to 862 MHz (KCMTS-122E) |
| Signal Level | 50 to 61 dBmV, adjustable at 0.5 dB steps |
| Channel Bandwidth | 6 MHz (KCMTS-122), 8MHz (KCMTS-122E) |
| Symbol Rate (nominal) QAM64 QAM256 | KCMTS-122: KCMTS-122E 5.056941 Msym/sec 6.952 Msym/sec 5.360537 Msym/sec 6.952 Msym/sec |
| Frequency Response | ~ 18% Square Root Raised Cosine shaping ~ 12% Square Root Raised Cosine shaping |
| Spurious and Noise Inband discrete (fc +/- 3MHz) Inband spurious & noise (fc +/- 3MHz) Adjacent channel (fc +/- 3 MHz) to (fc +/- 3.75 MHz) (fc +/- 3 MHz) to (fc +/- 9 MHz) Next adjacent channel (fc +/- 9 MHz) to (fc +/- 15 MHz) Other channels 47 MHz to 1,000 MHz | KCMTS-122: < -57 dBc in 6 MHz < -48 dBc in 6 MHz; where channel spurious and noise includes all discrete spurious, noise, center leakage, clock lines, synthesizer products, and other undesired transmitter products. Noise with +/- 50 KHz of the carrier is excluded. < -58 dBc in 750 KHz < -62 dBc, in 5.25 MHz, excluding up to 3 spurs, each of which must be -60 dBc when measured in a 10 KHz band < -65 dBc in 6 MHz < -12 dBmV in each 6 MHz channel |
| Phase Noise | 1 KHz to 10 KHz: -33 dBc double sided noise power 10 KHz to 50 KHz: -51 dBc double sided noise power 50 KHz to 3 MHz: -51 dBc double sided noise power |
| Output impedance | 75 Ohms |
| Output Return Loss | > 14 dB with an output channel up to 750 MHz; > 13 dB in an output channel above 750 MHz |
| Connector Type | F type |

KCMTS-122, KCMTS-122E Specifications (continued)

| Upstream Physical Layer |
| --- |
| Quantity of downstream channel | 2 |
| Modulation type | Burst (TDMA) QPSK and QAM16 |
| Frequency Range | 5 to 42 MHz (KCMTS-122) 5 to 65 MHz (KCMTS-122E) |
| Tuning Resolution | 1 Hz |
| Level Range (one channel) | 160 Ksps: -16 to +14 dBmV 320 Ksps: -13 to +17 dBmV 640 Ksps: -10 to +20 dBmV 1.28 Msps: -7 to +26 dBmV 2.56 Msps: -4 to +26 dBmV |
| Total Input Power | Not to exceed + 35 dBmV (95dBuV) |
| Burst Length | 1 to 255 minislots Minislot size from 6.25 to 800 us |
| FEC Coding | Variable burst to burst: Reed-Solomon T = 1 to 10 or 0 (off) Codeword size 16 to 255 bytes |
| Randomizing | Burst Synchronous, programmable seed |
| Symbol Rate (nominal) | 160, 320, 640, 1,280 and 2,560 Ksym/sec |
| Bandwidth | 200, 400, 800, 1,600 and 3,200 KHz (-30 dB, 25% SRRC) |
| Equalization | Decision Feedback, 5 taps FF, 4 taps FB |
| Connector Type | F type |

| MAC Layer |
| --- |
| Upstream Forwarding Rate | 17 K packets/sec max 10 Mpbs (limited by upstream modulation type chosen) |
| Downstream Forwarding Rate | KCMTS-122 64 QAM: 50K packets/sec or 28 Mbps 256 QAM: 66K packets/sec or 38 Mbps |
| Broadcast Packet Forwarding Rate | Limited to 1000 packets/sec to guard against denial of service attacks. |
| Media Service Access Point (MSAP) | 1 MSAP to 8190 MSAP Unicast Service IDs 100 Multicast Service IDs |
| CM Support | Up to 512 |
| CPE Support | Up to 8192 CPEs. Up to 16 CPE devices per CM. |
| CM Registration Filtering | Reject or exclusively accept up to 5 sets of CM Ethernet address ranges. |
| Minimum MAP Time Interval | 2 ms |
| Downstream QoS | DOCSIS rate limiting method. Elastic buffering of up to 800 ms total downstream data. |
| Ethernet Address Forwarding | Support for 32768 IDs. |
| Upstream Packet Concatenation | Supported |
| Upstream Piggyback Requests | Supported |
| Maximum CM Distance setting | Decrease upstream latency for CM data. |

KCMTS-122, KCMTS-122E Specifications (continued)

| AC Power |
| --- |
| Parameter | Typical Value | Maximum Value |
| Nominal Input Voltage | 115V to 240V |  |
| Input Voltage Tolerance |  | +/- 10% |
| Input Frequency | 50 Hz / 60 Hz |  |
| Input Frequency Tolerance |  | +/- 2% |
| Input Power | 150 W |  |

| Mechanical |
| --- |
| Configuration | 19 inch rack or table/tray mount |
| Dimension | 3.5” H (2 RU) x 17.2” W (18.25” with rack mounting flanges) x 12.7” D |
| Weight | 16 lbs rack mounted |
| Shipping Weight | 23 lbs |

| Environmental |
| --- |
| Operating Temperature Range | 0oC to 50oC |
| Storage Temperature Range | -40oC to -125oC |
| Operating Humidity | 10% to 90% non-condensing |